## Slide 1
APEEJAY STYA UNIVERSITY
Internet of Things & Its Applications
BCA 2nd Year | 4th Semester

## Slide 2
TEAM MEMBERS
1
Shubham Kumar
Team Lead / Hardware / Coding
2
Vishwash Anand
Arduino Programming
3
Khushi
Circuit Design
4
Ritika
Documentation
5
Naitik
Mechanical Assembly
6
Krish
Sensor Integration
7
Tema
Testing & QA
8
Ochen
Power Management
9
Caleb
Presentation Design
10
Roshan Kumar
Research & Analysis

## Slide 3
Variable Head
Grass Cutter Weed Trimmer
Arduino UNO
L293D Shield
BLDC Motor
Ultrasonic Sensor
IoT Based
Auto Navigation

## Slide 4
INTRODUCTION
🤖 WHAT IS THIS ROBOT?
An autonomous IoT-based robot designed to cut grass and weeds automatically
Built on Arduino UNO microcontroller platform
Uses ultrasonic sensors to detect obstacles and change direction automatically
Powered by a BLDC (Brushless DC) motor for high-speed blade rotation
4-wheel drive using Johnson DC Geared Motors (200 RPM)
Variable head allows adjustable cutting height
🎯 PROJECT OBJECTIVES
Automate grass cutting
Reduce human effort in garden maintenance
Obstacle avoidance
Auto-detect and navigate around obstacles
IoT Integration
Smart monitoring and control via IoT
Variable head height
Adjustable blade for different grass types
Cost effective
Low-cost components, high impact project

## Slide 5
COMPONENTS USED
1x
Arduino UNO R3
Main Microcontroller — Brain of robot
1x
L293D Motor Driver Shield
Controls 4 DC motors direction & speed
4x
Johnson DC Gear Motor 12V
4-wheel drive movement (200 RPM)
1x
BLDC Brushless DC Motor
High-speed grass cutting blade motor
1x
Ultrasonic Sensor HC-SR04
Obstacle detection (TRIG→A0, ECHO→A1)
1x
SG90 Servo Motor
Head pan motion — left/right scanning
1x
ESC + Servo Tester
Controls BLDC motor speed & on/off
1x
LiPo Battery (11.1V)
Main power supply for entire robot
4+1x
Wheels (Large + Medium)
Traction and movement on grass
1x
Wooden Frame
Robot body/chassis construction
Set
Ribbon Wires
All internal circuit connections
4x
4x Cutting Blade
Attached to BLDC motor for grass cutting

## Slide 6
CONNECTION DIAGRAM
🔋 BATTERY
11.1V LiPo
14000mAh
⚡ ARDUINO UNO R3
D1-D4: Motor Control D10: Servo Motor (PWM) A0 (TRIG) / A1 (ECHO): Ultrasonic 5V Regulator onboard
L293D MOTOR DRIVER SHIELD
M1 M2 M3 M4 → 4 DC Motors
Servo Port D9/D10 → SG90
Mounted ON Arduino UNO
Stacked
DC GEAR MOTORS
4x Johnson 12V
200 RPM
M1, M2, M3, M4
(4-Wheel Drive)
M1-M4
ULTRASONIC SENSOR
TRIG → A0 (Arduino)
ECHO → A1 (Arduino)
VCC=5V, GND
A0/A1
SG90 SERVO
PWM → D10
Head pan motion
180° rotation
D10
BLDC MOTOR
100KV Motor
→ ESC Module
→ Servo Tester
Direct 11.1V
4x Blades
ESC/
Servo Tester
11.1V Power

## Slide 7
PIN CONNECTION TABLE
Component | Pin/Port | Arduino Connection | Purpose
L293D Shield | Motor Shield | Stacked on top of UNO | Controls motor direction & speed
DC Motor 1 (FL) | M1 Port | L293D Shield M1 | Front-Left wheel drive
DC Motor 2 (FR) | M2 Port | L293D Shield M2 | Front-Right wheel drive
DC Motor 3 (RL) | M3 Port | L293D Shield M3 | Rear-Left wheel drive
DC Motor 4 (RR) | M4 Port | L293D Shield M4 | Rear-Right wheel drive
Ultrasonic TRIG | TRIG Pin | Arduino A0 | Sends ultrasonic pulse
Ultrasonic ECHO | ECHO Pin | Arduino A1 | Receives reflected pulse
SG90 Servo | PWM Signal | Arduino D10 (PWM) | Head pan for obstacle scan
BLDC Motor | 3-wire | ESC → Servo Tester → Battery 11.1V | High-speed cutting blade
Battery 11.1V | VCC / GND | EXT_PWR on Shield | Powers full robot
ESC Module | Signal Wire | From Servo Tester | Speed control of BLDC

## Slide 8
HOW IT WORKS
01
Power ON
11.1V LiPo battery powers Arduino UNO & all components through the L293D shield
02
Initialize
Arduino starts, sets up motor pins D1-D4, servo on D10, ultrasonic on A0/A1
03
Start Moving
4 DC motors (200 RPM) drive the 4 wheels forward. BLDC motor spins blades at high speed
04
Obstacle Detection
Ultrasonic sensor fires pulse every loop. If object < 20cm, robot stops and servo scans left/right
05
Direction Change
Based on scan result, Arduino commands motors to turn left/right. Robot continues cutting
🔁 Loop repeats continuously — robot auto-navigates and cuts grass until battery is depleted or manually stopped

## Slide 9
ARDUINO CODE OVERVIEW
// LIBRARIES & SETUP
#include <AFMotor.h>
#include <NewPing.h>
#include <Servo.h>
#define TRIG A0
#define ECHO A1
#define MAX_DIST 200
AF_DCMotor motor1(1); // Front-Left
AF_DCMotor motor2(2); // Front-Right
AF_DCMotor motor3(3); // Rear-Left
AF_DCMotor motor4(4); // Rear-Right
NewPing sonar(TRIG, ECHO, MAX_DIST);
Servo myservo;
void setup() {
myservo.attach(10); // SG90 on D10
myservo.write(90); // Center position
motor1.setSpeed(150);
motor2.setSpeed(150);
motor3.setSpeed(150);
motor4.setSpeed(150);
}
// MAIN LOOP LOGIC
void loop() {
int dist = sonar.ping_cm();
if (dist > 20 || dist == 0) {
// Move Forward
motor1.run(FORWARD);
motor2.run(FORWARD);
motor3.run(FORWARD);
motor4.run(FORWARD);
} else {
// Stop all motors
motor1.run(RELEASE);
motor2.run(RELEASE);
motor3.run(RELEASE);
motor4.run(RELEASE);
delay(500);
// Scan with servo
myservo.write(30); // Look Right
delay(500);
int distR = sonar.ping_cm();
myservo.write(150); // Look Left
delay(500);
int distL = sonar.ping_cm();
if (distR > distL) { // Turn Right
motor1.run(FORWARD);
motor2.run(BACKWARD);
} else { // Turn Left
motor1.run(BACKWARD);
motor2.run(FORWARD);
}
delay(400);
}
}

## Slide 10
WHY EACH COMPONENT?
Arduino UNO R3
Most popular open-source microcontroller. Easy to program via Arduino IDE. Has enough digital/analog pins for all components. 5V onboard regulator.
L293D Motor Driver Shield
Controls 4 DC motors simultaneously using H-bridge. Directly stacks on Arduino. Supports forward/backward direction using AFMotor library.
200 RPM Johnson DC Motor
12V geared motor provides torque for movement on grass/uneven terrain. 200 RPM is ideal for stable, controllable movement.
BLDC Brushless DC Motor
Extremely high rotation speed needed to cut grass. Brushless = longer life, less heat, more efficient. Perfect for cutting blade.
Ultrasonic Sensor HC-SR04
Non-contact obstacle detection up to 4m. Uses sound waves. Connected to A0/A1 for real-time distance measurement via NewPing library.
SG90 Servo Motor
Small, lightweight servo for scanning the ultrasonic sensor left and right. Controlled by D10 PWM pin. 180° rotation range.
ESC + Servo Tester
Electronic Speed Controller regulates BLDC motor power. Servo Tester manually controls speed. Runs directly on 11.1V battery.
11.1V LiPo Battery
Lithium Polymer batteries are lightweight and provide high current. 14000 mAh = long runtime. Powers both logic (via 5V reg) and motors.

## Slide 11
REFERENCES
01
Product Reference
Harish Projects — Automatic Grass Cutter Robot Kit
https://harishprojects.com/products/automatic-grass-cutter-robot-for-garden-science-project-kit
02
Video Reference
YouTube — Automatic Grass Cutter Robot Build Tutorial
https://www.youtube.com/watch?v=O6o59ZgZq6I
03
Technical Guide
How2Electronics — Automatic Grass Cutting Robot using Arduino
https://how2electronics.com/make-an-automatic-grass-cutting-robot-using-arduino/
04
Code Library
AFMotor Library — Adafruit Motor Shield Library (GitHub)
https://github.com/adafruit/Adafruit-Motor-Shield-library
05
Code Library
NewPing Library — Ultrasonic Sensor Library (GitHub)
https://github.com/microflo/NewPing
06
Platform Reference
Arduino Official Documentation — arduino.cc
https://www.arduino.cc/reference/en/

## Slide 12
THANK YOU!
Variable Head Grass Cutter Weed Trimmer Robot
BCA 2nd Year | 4th Semester | IoT & Its Applications
APEEJAY STYA UNIVERSITY